## Slide 1
Artificial Intelligence and Machine Learning for Direction of Arrival (DOA) Estimation
Work Update
Tamal Bose, RMS
April 17, 2020
This document (or software if applicable) contains data whose export/transfer/disclosure is restricted by U.S. law. Dissemination to non-U.S. persons whether in the United States or abroad requires an export license or other authorization.

## Slide 2: [1] Neural Network-Based Adaptive Beamforming for One- and Two-Dimensional Antenna Arrays A. H. El Zooghby, C. G. Christodoulou, and M. Georgiopoulos IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, VOL. 46, NO. 12, DECEMBER 1998
Adaptive Beamforming using neural networks
Computation of the optimum weights is accomplished using 3-layer radial basis function neural networks (RBFNN)
The results obtained from this network are in excellent agreement with the Wiener solution
Examples include ULA (10x1) and URA (8x8 and 10x10)

## Slide 3: [2] Least Squares Support Vector Machines for Direction of Arrival Estimation Judd A. Rohwer, Chaouki T. Abdallah, and Christos G. Christodoulou IEEE Proc. Antennas and Propagation, 2003
DoA estimation using SVM
Uses Decision Directed Acyclic Graph approach for LS-SVM
Actual simulation results not given
Very poorly written paper

## Slide 4: [3] Direction of Arrival Estimation Based on Support Vector Regression: Experimental Validation and Comparison With MUSIC A. Randazzo, M. A. Abou-Khousa, M. Pastorino, and R. Zoughi IEEE ANTENNAS AND WIRELESS PROPAGATION LETTERS, VOL. 6, 2007
Estimating the directions of arrival (DOAs) of coherent electromagnetic waves impinging upon a uniform linear array (ULA) is considered.
An efficient DOA estimation approach based on the support vector regression is assessed.
The results are compared with those yielded by the multiple signal classification (MUSIC) algorithm
Experiments performed with one source and long ULA. Even so, accuracy not that good when compared to MUSIC.

## Slide 5: [4] A Neural Network-Based Smart Antenna for Multiple Source Tracking Ahmed H. El Zooghby, Christos G. Christodoulou, and Michael Georgiopoulos IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, VOL. 48, NO. 5, MAY 2000
Multi-source DoA and tracking using neural network
The neural multiple-source tracking (N-MUST) algorithm is based on an architecture of a family of radial basis function neural networks (RBFNN) to perform both detection and direction of arrival (DOA) estimation
Simulation results are quite good and shown for DoA and for tracking
Used 8-element array and 4 sources
Also used 4-element array with 8 sources. Works well in this case as well. Interesting!
Quote: “The ability of the network to determine the angles of arrival of a number of sources that is greater than the number of array elements M may be interpreted by the fact that unlike signal subspace based algorithms, (e.g., MUSIC algorithm) no eigen-decomposition is necessary and no search is performed in a subspace with dimension less than M.”

## Slide 6: [5] Direction-of-Arrival Estimation Based on Deep Neural Networks With Robustness to Array Imperfections Zhang-Meng Liu , Chenwei Zhang, and Philip S. Yu IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, VOL. 66, NO. 12, DECEMBER 2018
A framework of the deep neural network (DNN) to address the DOA estimation problem, so as to obtain good adaptation to array imperfections and enhanced generalization to unseen scenarios
The framework consists of a multitask autoencoder and a series of parallel multilayer classifiers
The autoencoder acts like a group of spatial filters, it decomposes the input into multiple components in different spatial subregions
Simulations performed with 10-element ULA with 2 and 3 sources
Simulations performed with different kinds of array imperfections as well, exhibiting promising results

## Slide 7: [6] EFFICIENT NEURAL NETWORK APPROACH FOR 2D DOA ESTIMATION BASED ON ANTENNA ARRAY MEASUREMENTS Marija Agatonovi, Zoran Stankovi, Ivan Milovanovi, Nebojsa Doncov, Leen Sit, Thomas Zwick, and Bratislav Milovanovi Progress In Electromagnetics Research, Vol. 137, 741-758, 2013
An efficient Artificial Neural Network (ANN)-based model to estimate both azimuth and elevation arrival angles of a signal source.
The proposed model is capable to account for imperfections of measurement equipment as well as mutual couplings between array elements.
The neural model has been verified for several angular positions and frequencies.
It is shown that the use of ANN model to estimate angular positions of a signal source yields more accurate results when compared to 2D MUSIC.
The neural model significantly outperforms 2D MUSIC in terms of speed of computation.
Experiment with 4x4 array and 1 source.

## Slide 8: [7] Neural methods for antenna array signal processing: a review K.-L. Dua, A.K.Y. Laib, K.K.M. Chengb, M.N.S. Swamy Signal Processing 82 (2002) 547 – 561
A good survey on NN based antenna array processing
A survey of beamforming and DOA methods.
A survey of some popular NNs such as MP, Hopfield, RBF, PCA-net, Fuzzy NN, etc.
Discusses the advantages and disadvantages of using the different nets for beamforming and DOA.
Lots of references, but no simulation results.

## Slide 9: [8] Direction of Arrival Estimation by Using Artificial Neural Networks M.F Unlersen, E. Yaldiz 2016 European Modelling Symposium
ANN proposed for DOA using uniform linear arrays.
A simple NN with one hidden layer is trained using back propagation.
Training done using a 5-element ULA and 5 degree steps.
Results given for one source and two sources.
Pretty simple paper with little analysis.

## Slide 10: [9] Robust DOA Estimation Based on Convolutional Neural Network and Time-Frequency Masking Wangyou Zhang, Ying Zhou, Yanmin Qian INTERSPEECH 2019, Graz, Austria
This paper is for DOA for sound localization (not radar).
Uses CNN with time-frequency masking.
CNN with 3 convolutional layers and 3 fully connected layers.
Algorithms developed for CNN with and without T-F masking modules.
6-mic circular array.
Good results.

## Slide 11: [10] Neural network applications in smart antenna arrays: A review Abhishek Rawata, R.N. Yadavb, S.C. Shrivastava Int. J. Electron. Commun. (AEÜ) 66 (2012) 903– 912
Discusses different NNs for smart applications: Hopfield, MLP, RBF, etc.
RBFs are discussed for DOA and multiple source tracking.
Array synthesis using ANN and GA.
No simulation examples given.
Lots of references for these topics.
Nice table with types of NN and smart antenna application. This is probably the nicest part of the paper.

## Slide 12: [11] An Innovative Multiresolution Approach for DOA Estimation Based on a Support Vector Classification Massimo Donelli, Federico Viani, Paolo Rocca, and Andrea Massa IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, VOL. 57, NO. 8, AUGUST 2009
Uses SVM for DOA estimation.
The first step determines the decision function that correctly classifies whatever input pattern by means of a SVM-based approach.
In the second step, the output of the decision function is mapped into the a-posteriori probability that a signal impinges on the antenna from a fixed direction.
4x4 URA experiments with up to four incident signals.
Good results. Solid paper.

## Slide 13: [12] SPARSE BAYESIAN LEARNING FOR DOA ESTIMATION OF CORRELATED SOURCES Christoph F. Mecklenbrauker, Peter Gerstoft, and Geert Leus 2018 IEEE 10th Sensor Array and Multichannel Signal Processing Workshop (SAM)
The source amplitudes are assumed to be correlated zero-mean complex Gaussian distributed with unknown covariance matrix.
The DOAs and covariance parameters of plane waves are estimated from multi-snapshot sensor array data using sparse Bayesian learning (SBL).
Results given for 20-element array with 3 correlated sources.

## Slide 14: [13] Direction of arrival estimation for smart antenna in multipath environment using convolutional neural network Youssef Harkouss | Hassan Shraim | Hussein Bazzi International Journal of RF and Microwave Computer-Aided Engineering, 2018
Two main parts: DOA estimator and the switched-beam system.
DOA estimation: Based on convolutional neural network (CNN).
Don’t need to know the # source signals.
The CNN is capable to select the desired radiation beams of the switched-beam antenna without knowing the number of source signals, or if they are non-coherent or coherent signals.
Simulation results with 16-element array with two coherent or non-coherent signals.