## Slide 1: AI/ML Subspace-Based Parameter Estimation MPI Workshop 2025
6/9/2025
Al Samuel, Pranav Prabhakaran Sudha, Kevin Bongiovanni

## Slide 2: About Us: Raytheon Technologies (RTX)
Three main business units
  Collins Aerospace
    Specializes in advanced structures, avionics, interiors, mission systems, etc that serve the commercial, regional, business aviation and military sectors.
  Pratt & Whitney
    Designs, manufactures, and services advanced aircraft engines and auxiliary power systems for commercial, military and business aircrafts.
  Raytheon
    Design, development, manufacturing and sustainment concentrations in weapons, defense systems, and military and commercial electronics.
    67K+ Employees, 28K+ Engineers
    Team spread across 58 countries
    Worlds largest producer of guided missiles.
RTX Is A Global Provider Of Commercial And Defense Solutions
Raytheon Capabilities

## Slide 3: Description/Overview of Problem
Subspace based parameter estimation techniques, specifically Direction of Arrival Estimation (DoA), are well understood and prominent in signal processing.
  Techniques include MUSIC, ESPRIT, and Matrix Pencil algorithms
  Exploit inherent orthogonality that exists between noise subspace and signal vectors that span the (signal+noise) subspace
    Noise subspace-based projection matrices are used by algorithms
AI/ML approaches have been developed that derive surrogate matrices which behave like noise subspace-based projection matrices.
A brief analysis showed that these surrogate matrices behave like an interesting cross between beamforming and noise subspace projection matrices.
These surrogate matrices may serve as a basis for developing virtual sensor concepts.
Understand Properties of AI/ML Surrogate Matrices and Potentially Develop Additional Surrogates

## Slide 4: Goals for Problem Solvers
Deeper Understanding of AI/ML Surrogate Matrix Bolsters Confidence in Solution
Goal 1: Characterize AI/ML Surrogate Matrix
Develop an understanding of its mathematical properties
Identify relations to MUSIC noise subspace or MVDR inverse matrix.
Determine how surrogate matrix is able to demonstrate enhanced behavior
Goal 2: Derive Additional Surrogate
Matrices
Exploit and enhance any understood principles of the AI/ML surrogate matrix.
Leverage surrogate matrices to develop virtual sensor concepts that provide enhanced degrees of freedom

## Slide 5: Overview of Presentation
Discussion Topics
Antenna Arrays and Correlation Matrices
Direction of Arrival Estimation
  Conventional Beamforming
  MVDR
  MUSIC
    Subspaces and Orthogonality
    Eigendecomposition
Neural Networks for DoA Estimation
  Model-Based Networks
  COSnet
Revisit Problem Statement
  Provided Data

## Slide 6: Antenna Arrays and Correlation Matrices

## Slide 7: Antenna Array: The What and Why
A set of multiple connected antennas (sensors/elements) that work together as a single antenna.
Why Use an Antenna Array?
  Provides Directivity
  Achieves Higher Gain
  Allows for Direction Finding
Antenna Arrays are Critical for RF Direction Finding
PAVE PAWS (Phased Array Warning System), a complex Cold War early Warning Radar System developed in 1980 utilizing a pair of Raytheon AN/FPS-115 phased array radars, each having 2,677 antenna elements.
Linear Folded Dipole Antenna. Omnidirectional in azimuth (horizontal) but directive in elevation (vertical). Used for dispatch services.,
The Very Large Array (VLA) Y-shaped array of 27 Dish Antennas. Built by National Radio Astronomy Observatory in Socorro, New Mexico for astronomical observations.
Example of Antenna Arrays
Normalized Antenna Patterns for ULAs
Mainlobe
Sidelobes
Cartesian Plot
Polar Plot

## Slide 8: Antenna Array: The Importance of Phase Delay
The received signal will vary in phase across an array
The phase difference between elements is due to a difference in propagation length
  and can be related to the angle of incidence
Estimating the rate of change in phase indicates the Direction of Arrival (DoA) of the signal.
The Phase Delay Between Elements is Related to The Direction of Arrival
Wavefront Signal
Antenna Array
(aperture)
Phase Delay Between Elements Separated by
Incidence of Received Wavefront On Antenna Array

## Slide 9: Antenna Array: A Mathematical Data Model
Consider a Uniform Linear Array (ULA) in 1-D Angle Space
  All elements are identical in terms of radiation pattern, orientation, etc.
The expression for the complex array output, x , due to the incidence of M far-field signals (sources) is
ULA Antenna Receive Data Model is Established
Complex Signal Coefficient
Noise Vector
Steering Vector
where
Uniform Element Spacing
(as a multiple of λ)
Incident Angle
Matrix Notation of Received Signal of Array
Wavefront from Scatter
Wavefront from Scatter
⇒
boresight

## Slide 10: Spatial Correlation Matrix
Informs us how correlated the signal (and noise) is between any two sensors of our array.
Properties
  Square matrix of dim:
  Hermitian matrix
  Diagonal elements are real, representing powers
  Rank = #Independent Signals
In practice, we use multiple snapshots of array data to form a Estimated (Sample) Correlation Matrix.
Spatial Correlation Matrices are Important for Array Signal Processing
}
True Correlation Matrix
Estimated Correlation Matrix
where are K independent array output observations, or snapshots.
approaches , the true correlation matrix, as K increases.
Consider a sample of the array output as
where
Ergodicity

## Slide 11: Direction of Arrival Estimation
Methods for

## Slide 12: DoA Estimation: Importance and Practical Application
Goal
  Using the data received at the antenna array, estimate the angle of arrival of M signals
  Parameter that were estimating is
Methods
  Beamforming
  Subspace-based
  Stochastic/Deterministic ML
  Others
Challenges
  Unknown number of signals impinging on the array of unknown amplitude and mutual correlation
  Signals are corrupted by noise
  Generally assumed M < N (number of sensors) but not always true.
DoA Estimation is Used Across Numerous Domains, Several Approaches to Estimation
Radar
Wireless Communications
Navigation
Radio Astronomy
Seismology
Sonar
Applications of Direction Finding in Various Domains

## Slide 13: Conventional Beamforming
Theory
Beamforming is an operation that creates a spatial filter; it filters out signals from all directions except the desired one.
Used to
  Increase SNR of desired signals
  Null out interferers
  Shape beam patterns
  Basic DoA Estimation
Involves choosing weight vector,w , that maximize array gain in intended direction.
DoA Estimation is performed by applying chosen weight vector to array data for all DoAs of interest.
Limitations
Resolution is tied to beamwidth of antenna. Can't resolve multiple sources within beamwidth.
Doesn’t work well when noise is high.
Simple Approach to DoA Estimation, Poor Resolution
Determining Weight Vector
Performing Beamforming for DoA Estimation
We need the weight vector to
Adjust the phases of the array data so that the signal constructively adds up in a desired direction
Have a magnitude of 1
The steering vector satisfies these conditions!
Scan through all DoAs within the angular region of interest. For each DoA, ,
  Use the conventional beamformer to determine weights,
  Apply weight to array data,
    This is the magnitude of the beamformed signal at the DoA of
Beamformer for Two Well-Separated Sources*
Beamformer for Two Closely-Separated Sources*
Sources are Resolvable
Sources are Unresolvable
* Using a 6elem. ULA

## Slide 14: MVDR: Minimum Variance Distortionless Response
Also known as the Capon DoA Estimator
Can be used for both beamforming and DoA
Scans an MVDR beam over the angular region of interest
  A form of adaptive beamforming
Can resolve sources more closely than a conventional beamformer
  Example of Superresolution
Limitations
Very sensitive to sensor errors
Has a lower spatial resolution than MUSIC
An Adaptive Beamformer With Improved Resolution Compared to Conventional Beamforming
Determining MVDR Beamformer Weight Vector
Gain = 1
Minimize Variance Or Expected Value of Power
}
Noise Correlation Matrix
subject to
Performing MVDR Beamforming for DoA Estimation
Using Beamformer Weights: Scan through all DoAs within the angular region of interest. For each DoA, , apply the MVDR weights
Using Spectral Approximation: A simplified expression for the power spectrum generated by using MDVR weights is
Comparing MVDR to Conventional Beamforming*
* Using a 6elem. ULA
In practice, is used instead of

## Slide 15: MUSIC: Multiple Signal Classification
Theory
  All N eigenvectors of are orthogonal
  The smallest eigenvalues are identical. Their corresponding eigenvectors form the noise subspace, .
  The eigen vectors corresponding to the remaining M largest eigenvalues form the signal subspace, .
  is orthogonal to ( )
  If a signal vector , then
  To measure the orthogonality of w.r.t , MUSIC defines the squared norm
    Orthogonality is satisfied when 0
    is the noise projection matrix
  MUSIC defines its angular estimation function (pseudo-spectrum) as
    where is the candidate steering vector for a particular DoA.
  The locations of the peaks of give us the DoA estimates.
Limitations
  K (#snapshots) > N (dim.of / # of sensors)
Exploitation of Orthogonality of Signal Vectors to Noise Subspace Allows for Accurate Estimation
Eigenvalues of Sample Correlation Matrix
Eigenvectors of Sample Correlation Matrix
Signal Subspace
Noise Subspace
For a sample correlation matrix, , the eigendecomposition provides us the diagonal eigenvalue matrix and the square eigenvector matrix Q
Note: the sample correlation matrix, , contains information of both the Signal and Noise Subspace

## Slide 16: MUSIC: Algorithm and Limitations
MUSIC is Powerful But Has Its Limitations
  Perform an eigen decomposition of
  Determine the size of the signal and noise subspace by looking at the eigenvalues (AIC/MDL Algorithms).
  Determine the noise subspace UN.
  Search over steering vectors to find ones which are orthogonal to the noise subspace (find peaks of ).
Dominant eigenvalues corresponding to number of signals ()
eigenvalues corresponding to noise
Algorithm Description
Advantages
Limitations
Exploits orthogonality of noise subspace and signal vectors
Has the superresolution ability, i.e. estimating multiple sources within the mainlobe of the antenna pattern
Converges to true DoA as #snapshots increases
Requires estimation of number of signals
Assumes #sources < #sensors ( M < N )
Assumes sources to be uncorrelated

## Slide 17: Neural Networks for DoA Estimation

## Slide 18: Overview of Neural Networks for DoA Estimation
Neural networks are universal approximators
  Given a continuous function and some , there exists a neural network with a single hidden layer such that
Deep networks with many layers and have shown strong, potentially unlimited discriminative power
Utilizing N.N.s for DoA Estimation
A mapping can be defined
  between the DoA values and the array data x
Neural Networks Have Wide Applicability in Signal Processing
Basic Perceptron (Neuron) Operation
Example of a Deep Neural Network
The DoA Estimation problem is defined as the retrieval starting from the knowledge of x , as seen in the inverse mapping
AI/ML, more specifically Neural Networks, can be used to estimate this inverse mapping.

## Slide 19: Model Based Deep Learning
Model Based Deep Learning Combines The Benefits of Both Approaches

## Slide 20: COSnet: Complex Orthogonal Search Network
COSnet “Learns” a Surrogate Matrix That Behaves Like the Noise Subspace Based Projection Matrix
Network Architecture
Input
Dim:
(N x N x 1)
Sample Correlation Matrix from a N-Element ULA (complex)
Trainable Layers
Dim:
(N x N x 1)
Arbitrary number/dimension of hidden layers
Learned Output of Final Hidden Layer
Fixed Layers
Assess orthogonality against steering vectors in set A
Performs reciprocal operation and converts output to be dB-like
This network attempts to loosely replicate the orthogonal search performed by MUSIC to find steering vectors which are orthogonal to the noise subspace.
We will refer to the term as which is the learned surrogate matrix.
Output
Estimated Spatial Spectrum by Network
Dim:
( x1)
Comparison of Estimated Spatial Spectrum Made by COSnet Using Surrogate Matrix vs MUSIC
Surrogate Matrix

## Slide 21
Comparison of MUSIC Algorithm to Model Based Deep Learning Approach
Network Architecture
Input
Dim:
(N x N x 1)
Sample Correlation Matrix from a N-Element ULA (complex)
Trainable Layers
Dim:
(N x N x 1)
Arbitrary number/dimension of hidden layers
Learned Output of Final Hidden Layer
Fixed Layers
Assess orthogonality against steering vectors in set A
Performs reciprocal operation and converts output to be dB-like
Output
Estimated Spatial Spectrum by Network
Dim:
( x1)
Surrogate Matrix
MUSIC Algorithm
Input
Dim:
(N x N x 1)
Sample Correlation Matrix from a N-Element ULA (complex)
Dim:
(N x N x 1)
Noise Subspace Based Projection Matrix
Assess orthogonality against steering vectors in set A
Performs reciprocal operation
Output
Estimated Spatial Spectrum by Algorithm
Dim:
( x1)
Surrogate Matrix
Eigendecomposition into

## Slide 22: COSnet: Capabilities
AI/ML Surrogate Matrix Has Additional Capabilities and Flexibility in Its Structure/Nature
MUSIC can theoretically predict up to (N-1) sources for N spatial degrees of freedom( # of antenna elements)
(Left) The learned Xn surrogate matrix produced by COSnet shows the ability to resolve up to N sources.
Resolving up to N Sources
Additional information can be provided to the neural network as input to improve predictive ability
(Right) Providing a Quadricovariance matrix as input to the COSnet showed enhanced resolution of N sources, but did not expand the DoFs.
Utilizing Alternative Input Data
* Using a 4elem. ULA
* Using a 4elem. ULA

## Slide 23: Restate Problem Statement

## Slide 24: Goals for Problem Solvers
Various Surrogate Matrices Have Been Covered. Can We Develop A Better One?
Goal 1: Characterize Surrogate Matrix
Understand its mathematical properties
Identify relations to MUSIC noise subspace or MVDR inverse matrix.
Determine how surrogate matrix is able to demonstrate enhanced behavior
Goal 2: Derive Additional Surrogate
Matrices
Exploit and enhance any understood principles of the surrogate matrix.
Leverage surrogate matrices to develop virtual sensor concepts that provide enhanced degrees of freedom
Surrogate Matrices | MVDR | MUSIC | COSnet
Surrogate Matrices | MVDR | MUSIC | COSnet

## Slide 25: Provided Data
Continued Support For Providing Any Required Data/Scripts/Information
Surrogate Matrix Data
Algorithm/Helper Scripts
References
50 Realizations of Array Data for each source count (1-4) that Includes
Normalized Sample Correlation Matrix
: Corresponding AI/ML Surrogate Matrix
: Truth DoAs of sources
: SNRs of sources
General ULA parameters (ne, d, az_extent)
MATLAB script to support analysis of data and methods
Plot Antenna Pattern of ULA
Generate Steering Vectors
Form Array Output Data
Demonstration Algorithms
  Conventional Beamformer
  MVDR Beamformer
  MUSIC
Load Surrogate Matrix Data and Plot Spatial Spectrum.
Papers on MUSIC and other Subspace Based Techniques
R. Schmidt, “A signal subspace approach to multiple emitter location and spectral estimation”,
2. R. H. Roy, “ESPRIT – Estimation of Signal Parameters via Rotational Invariance Techniques”,
3. Y. Hua and T. K. Sarkar, “Matrix Pencil Method for Estimating Parameters of Exponentially damped/Undamped Sinusoids in Noise”, IEEE Transactions on ASSP, Vol. 38, No. 5, May 1990
4. T. K. Sarkar and O. Pereira,” Using the Matrix Pencil Method to Estimate the Parameters of a Sum of Complex Exponentials”, IEEE AP Magazine, Vol. 37, No. 1, February 1995.
Papers on Higher Order Statistics and Virtual Array Concepts
B. Porat and B. Friedlander, “Direction finding algorithms based on high-order statistics,” IEEE Trans. Signal Processing, vol. 39, 2016-2024, Sep. 1991.
2. M. C. Dogan and J. M. Mendel, “Applications of cumulants to array processing: I. Aperture extension and array calibration.” IEEE Trans. Signal Proc., vol. 43, pp. 1200-16, May 1995.
3. P. Chevalier, L. Albera, A. Ferreol, and P. Comon, “On the virtual array concept for higher order array processing,” IEEE Trans Signal Processing, vol. 53, pp. 1254-1271, Apr. 2005.
4. P. Chevalier and A. Ferreol, “On the virtual array concept for the fourth-order direction finding problem,” IEEE Trans. Signal Processing, vol. 47, pp. 2592-2595, Sep. 1999.

## Slide 26: Questions?
Thank you!

## Slide 27: Quadricovariance Matrix
) / K
+ ) / 2
Forming Quadricovariance Matrix